## Slide 1: Seasonal Heat Pump Data Clustering
Chart: Spring typical daily load profile
Cluster | Probability | Customers
0 | 0.7834 | 1469
1 | 0.2165 | 407
Chart: Summer typical daily load profile
Cluster | Probability | Customers
0 | 0.8015 | 1519
1 | 0.1985 | 377
The optimal number of clusters is 2 for both Spring and summer.
Cluster probability = customer within this cluster / total customers.
The typical daily load profile is the centroid (mean) of data within each cluster.
Notes: The cluster probability is used to sample the data later when we calculate the transformer loading condition and hosting capacity using Monte Carlo simulation. Data will be randomly picked from those clusters based on this probability.

## Slide 2: Seasonal Heat Pump Data Clustering
The optimal number of clusters is 2 for Fall and 4 for summer.
Cluster probability = customer within this cluster / total customers.
Chart: Fall typical daily load profile
Cluster | Probability | Customers
0 | 0.9288 | 1760
1 | 0.07115 | 136
Chart: Winter typical daily load profile
Cluster | Probability | Customers
0 | 0.242 | 461
1 | 0.085 | 160
2 | 0.644 | 1219
3 | 0.0299 | 56
Notes: The clustering is effective because we can distinguish the curve very clearly, which means that there is a significant difference between each subset.